## Slide 1: Geometry Homography & SFM
Class 5-6

## Slide 2: Today
Stereo:
  Rectification, matching, other stereo pairs
Special cases:
  planar surfaces, camera rotation
Structure from motion (SFM)
Tools:
  Homography transformation, RANSAC, SVM

## Slide 3: Rectification
Simplify the use of epipolar lines
Cl
Cr
P
pl
u
pr

## Slide 4: Rectification
Let A and B be 33 non singular matrices.
Transform the left image by L
Transform the right image by R=B R
Choose A and B such that F’=A-TFB-1 is a pure translation:

## Slide 5
Taken from: SYNTIM-INRIA.
Rectification

## Slide 6: More on Correspondence

## Slide 7: Correspondence
Similarity of patches
Geometric constraints:
  Epipolar geometry
Global constraints:
  Shape smoothness
  Order preserving
  ..

## Slide 8: Points Attribute Constraints
A pair of corresponding points must have the same physical origin
  Both are located on an edge due to a surface discontinuity, a shadow border, an occluding boundary, etc.

## Slide 9: Occlusion
+
+
Occluded in
Left Image
Occluded in
Right Image
Right
Left
Center of
projection
Center of
projection

## Slide 10: Uniqueness Constraint
Each pixel can correspond to at most one pixel in the other image
  No transparency
  No two or more points
  project to the same point

## Slide 11: Ordering Constraints
Corresponding points of similar depth typically maintain their order on the epipolar lines
  This assumption does not hold when there is a depth discontinuity
p
q

## Slide 12: Disparity Smoothness Constraint
The disparity changes slowly almost everywhere in the image
  True since the depth changes slowly almost everywhere in the 3D scene

## Slide 13: Mutual Correspondence Constraint
The existence of a correspondence between points does not depend on whether we start from the left image or the right image

## Slide 14: Correspondence Optimization
Local greedy matches:
  Low-level: Bottom up methods are based on local attributes of points
1D search
2D search:
  High-level: Minimizing an energy function that represents global and local properties of the surface (e.g., smoothness)

## Slide 15: High Level Energy Function
Assume rectified images:
Data Term
Regularization
weight
And

## Slide 16: 1D: Dynamic Programing
correspondence
p
q
Left occlusion
t
Right
occlusion
s

## Slide 17: Other Pairs of Images

## Slide 18: Mirrors
Taken from Mathieu and Devernay INRIA

## Slide 19: Structured Light
known camera and projector geometry
Depth can be recovered by triangulation

## Slide 20: Bilateral Symmetry

## Slide 21: Uncalibrated Stereo
Calibration is necessary to determine absolute 3D positions
We can determine relative 3D positions (up to a scale factor) without calibration

## Slide 22: What if we do not know the external parameters?
The disparity:
d =xl-xr
copl
copr
xl
xr
pl
pr
fl
fr=fl
T
Z
P
OL
Or

## Slide 23
A Priory Knowledge
Intrinsic and extrinsic parameters
Intrinsic parameters
No information about parameters
3D-Reconstruction From 2 Views
Unambiguous
Up to unknown scaling factor
Up to unknown projective transformation

## Slide 24: Stereo Summary
Triangulation
Correspondence
Epipolar geometry+ heuristics
Calibration
Remember: 3D reconstruction is possible only from 2 independent images

## Slide 25: Next
Homography
More than 2 images:
  Structure from motion
Other applications of Epipolar Geometry

## Slide 26: Homography

## Slide 27: Homography
A homography transformation: Let be corresponding points , where is a matrix
A pair of perspective images are related by an Homography transformation:
  Scene is a planar surface (proof: in class)
  The cameras are in the same location (identical up to rotation and intrinsic parameters)

## Slide 28: Homography
Computing the Homography
  Using the projection matrices (known plane)
  Using 4 corresponding points
  Using optical flow (later in the course)
Applications:
  Mosaics: stitching images together
  3D structure

## Slide 29: Plane-Induced Parallax: 3D Reconstruction
Decompose motion of scene points into two parts:
  2D homography (as if all points coplanar)
  Plane-induced parallax
Parallax: distance d relative to homography
d is proportional to
3D distance from plane
from Hartley & Zisserman

## Slide 30: Plane-Induced Parallax
Left view
Right view
Left view superimposed on right using homo-graphy induced by plane of paper
from Hartley & Zisserman

## Slide 31: Homography: Pure Rotation
31
virtual wide-angle camera
Taken from Jeffrey Martin

## Slide 32: Panoramas
Pick one image (red)
Warp the other images towards it (usually, one by one)
blend
Taken from Jeffrey Martin

## Slide 33: Multi-Camera Geometry
Multi-view stereo:
  Improve correspondence
  (e.g., use intersections of epipolar lines)
Structure from motion: more views but uncalibrated

## Slide 34: Structure From Motion

## Slide 35: Structure from Motion
Assumptions:
  A set of images
  Uncalibrated
Applications:
  Recover the camera locations
  Photo Tourism
  Improve robustness

## Slide 36: Structure from motion
Camera 1
Camera 2
Camera 3
R1,t1
R2,t2
R3,t3
p1
p4
p3
p2
p5
p6
p7
Slide by Seitz
Notes: Structure from motion solves the following problem:
Given a set of images of a static scene with 2D points in correspondence, shown here as color-coded points, find…
a set of 3D points P and
a rotation R and position t of the cameras that explain the observed correspondences. In other words, when we project a point into any of the cameras, the reprojection error between the projected and observed 2D points is low.
This problem can be formulated as an optimization problem where we want to find the rotations R, positions t, and 3D point locations P that minimize sum of squared reprojection errors f. This is a non-linear least squares problem and can be solved with algorithms such as Levenberg-Marquart. However, because the problem is non-linear, it can be susceptible to local minima. Therefore, it’s important to initialize the parameters of the system carefully. In addition, we need to be able to deal with erroneous correspondences.

## Slide 37: Structure from Motion
Given a sequence of images compute:
  The structure
  The motion (camera location)

## Slide 38: Application: Photo Tourism Overview
Scene reconstruction
Photo Explorer
Input photographs
Relative camera positions and orientations
Point cloud
Sparse correspondence
Photo Tourism: Exploring Photo Collections in 3D,
Snavely, Seitz, Szeliski
Slide by Seitz
Notes: Our system takes as input an unordered set of photos, either from an Internet search or from a large personal collection. We assume the photos are largely from the same static scene.
The first step of our system is to apply a computer vision techniques to reconstruct the geometry of the scene. The output of this procedure is the relative positions and orientation for the cameras used to take a connected set of the photographs, as well as a point cloud representing the geometry of the scene, and a sparse set of correspondences between the photos.
This information is then loaded into our interactive photo explorer tool.

## Slide 39: Photo Tourism Overview
Scene reconstruction
Photo Explorer
Input photographs
Slide by Seitz
Notes: Now I will describe the Photo Tourism system, beginning with the scene reconstruction procedure.

## Slide 40: Scene Reconstruction
Estimate
  Projection matrices: position, orientation, and focal length of cameras
  3D positions of feature points
Feature detection
Pairwise
feature matching
Structure from motion
(incremental or other)
Correspondence estimation
Slide by Seitz
Notes: Again, the goal of the reconstruction procedure is to automatically estimate the relative positions and orientations, as well as the focal length or zoom, of each of the photographs in a connected component of the scene. The process consists of four steps: detecting features in each of the input photos; matching features between each pair of photos; grouping the matches into correspondences across multiple photos; and using the correspondences to estimate the geometry of the scene and the cameras in a technique known as structure from motion.
I’ll now describe each of these steps in more detail.
[Structure from motion techniques for unordered image collections have also been developed by others, such as Brown and Lowe and Schaffalitzky and Zisserman, and the basic pipeline of our system closely follows that of Brown and Lowe. To our knowledge, our system is the first to have been demonstrated on large collections of photos from the Internet.]

## Slide 41: Feature Detection
Detect features using SIFT [Lowe, IJCV 2004]
Slide by Seitz
Notes: The core of the reconstruction process is the ability to reliably match feature points between images. Fortunately, over the last few years feature detection and matching techniques have improved dramatically. Many different technique exist – we use SIFT, or scale-invariant feature transform, developed by David Lowe. SIFT is designed to be invariant to image scale and rotation, as well as affine changes in image intensity.
Here is an image from the Trevi Fountain, and here are the features SIFT detects in the image, shown as square patches. The squares are scaled and rotated to reflect the scale and orientation of the features.

## Slide 42: Feature Detection
Detect features using SIFT [Lowe, IJCV 2004]
Slide by Seitz
Notes: So, we begin by detecting SIFT features in each photo.
[We detect SIFT features in each photo, resulting in a set of feature locations and 128-byte feature descriptors…]

## Slide 43: Feature Detection
Detect features using SIFT [Lowe, IJCV 2004]
Slide by Seitz

## Slide 44: Feature Matching
Match features between each pair of images
Slide by Seitz
Notes: Next, we match features across each pair of photos using approximate nearest neighbor matching.

## Slide 45: Feature matching
Refine matching using RANSAC [Fischler & Bolles 1987] to estimate fundamental matrices between pairs
Slide by Seitz
Notes: The matches are refined by using RANSAC, which is a robust model-fitting technique, to estimate a fundamental matrix between each pair of matching images and keeping only matches consistent with that fundamental matrix.
We then link connected components of pairwise feature matches together to form correspondences across multiple images.
Once we have correspondences, we run structure from motion to recover the camera and scene geometry. Structure from motion solves the following problem:

## Slide 46: Class 6
Continue SFM
Motion analysis (different set of slides)

## Slide 47: RANSAC
RAndom SAmple Consensus
An iterative method to estimate parameters of a model from a set of observed data which contains outliers, e.g.,
  A set of points a line
  A set of corresponding points fundamental matrix
  A set of corresponding points Homography

## Slide 48: RANSAC
Assumption:
  The model can be computed from a small set of points
  The set of points consists of inliers and outliers
Challenges:
  which points to use?
  When to stop?

## Slide 49: RANSAC
Iteratively selecting a random subset of points:
  Fit a model
  Test with the entire set: inliers and outliers
  Support set: sufficient large number of inliers
Repeat the model computation

## Slide 50: Correspondence Estimation
Run RANSAC
Compute set of correspondence, e.g., by:
  Use transitivity - connected components
  Use cliques
Image 1
Image 2
Image 3
Image 4
Slide by Seitz
Notes: The next step of our reconstruction algorithm is to link up matches between pairs of images into correspondences between multiple images, by finding connected components of matches. Suppose among these images, these features are matched only between consecutive pairs of images, perhaps because the scales of the images are so different. During correspondence estimation we link these matches and consider them to be 2D projections of a single 3D point in the scene.

## Slide 51: Affine Structure from Motion
The Problem:
Reconstruct scene geometry and camera motion from two or more images
Assumptions:
Known correspondence
Orthographic projection

## Slide 52: Affine Transformation
Translation, rotation, nonuniform scaling, shear
Parallel lines remain parallel
Lengths, areas, angles are lost

## Slide 53: Orthographic+ Scale Projection
Let P be an object point and p be an image point then , where
  R is a 3x3 rotation matrix
  s is a scale factor
  T is a translation vector
Define that is M is a 2x3 matrix
In this case , where b=MT

## Slide 55: Get Rid from Translation
Let pi0 be the projection of the object point P0 in image i
Translate all image points of image i : qij pij- pi0
We now have
instead of

## Slide 56: Tomasi - Kanade
A factorization algorithm to solve SFM
Based on SVD
Reference:
• Forsyth and Ponce book: Section 14.3
• Carlo Tomasi and Takeo Kanade, “Shape and motion from image streams under orthography: a factorization method,” International Journal of Computer Vision, 9(2):137-154, November 1992.

## Slide 58: Set Up
n unknown object points,
  3n unknowns
m unknown cameras,
  6m unknowns
mn known images of the object points
  2mn equations – non-linear!

## Slide 59: Ambiguity
Let Mi and Pj be a solution to
Let B be a non singular 3x3 matrix (affine transformation)
Mi’=MiB and Pj’=B-1Pj is also a solution

## Slide 60: Using Matrix Notation
Consider the set of projection of a point Pj into m images:
=
2mx1
2mx3

## Slide 61
Consider n points Pi
where
=
2mx3
2mxn
3xn
Ambiguity

## Slide 62: SVD: Singular Value Decomposition
Let A be an matrix with A=UDVT where:
U is an kk column orthonormal matrix
  UTU=I
D is a diagonal matrix,
V is an orthonormal matrix
VTV=I

## Slide 63: SVD
The columns of U, are the eigenvectors of AAT
The columns of V , are the eigenvectors of ATA
The elements of D, are the square roots of ATA eigenvalues (singular values)
  Which are the same as the square roots of and AAT
The singular values appear in decreasing order

## Slide 64: The Algorithm
Compute the singular value decomposition: Q=UDVT
Compute U3 ’ V3 and D3
M0=U3 and P0= D3 V3T
M0 is the camera motion estimation
  (2mx3 parameters)
P0 is the 3D point estimation
  (3n parameters)

## Slide 65: Questions
Can we choose a rigid solution?
What are the assumptions we made about the objects in the scene?
How can we solve the ambiguity?
How correspondence outliers expect to affect the algorithm?

## Slide 66: Incremental SFM
Slide by Seitz
Trevi Fountain,
Rome
Notes: To help get good initializations for all of the parameters of the system, we reconstruct the scene incrementally, starting from two images, then adding images one at a time. To begin, we automatically find a pair of images with many correspondences and which seem to have a large baseline, in order to get well-conditioned estimates of the parameters.
Here is the initial pair of images our system chose from the Trevi Fountain set. The images are similar enough to have a lot of features, but there is some distance between the cameras – the first camera is below the lip of the fountain and the second camera is above it. We first initialize these images to the origin…

## Slide 67: Incremental SFM
Optimize parameters for two cameras and common points
Find new image with most matches to existing points
Initialize new camera using pose estimation
Bundle adjust
Add new points
Bundle adjust
Slide by Seitz
Notes: and initialize the points observed by the images to a fixed depth from the cameras. We then run a non-linear optimization to refine the point locations and camera parameters.
Next, we add a new image to the optimization, choosing the image that observes the most existing 3D points. The parameters of the new camera are initialized using pose estimation, then a global refinement is run again. Finally, we add new points to the scene observed by at least two cameras using triangulation.

## Slide 68: Incremental SFM
Slide by Seitz
Notes: To help get good initializations for all of the parameters of the system, we reconstruct the scene incrementally, starting from two images, then adding a small number of images at a time.
Here’s a video of the incremental reconstruction of the Trevi Fountain photo set, starting from two cameras, and growing to a total of 350 cameras.
The process terminates when no more images has any matches to points in the scene.

## Slide 69: Perspective Projection: Incremental SFM
Slide by Seitz
Notes: To help get good initializations for all of the parameters of the system, we reconstruct the scene incrementally, starting from two photographs and the points they observe.

## Slide 70: Incremental SFM
Slide by Seitz
Notes: To help get good initializations for all of the parameters of the system, we reconstruct the scene incrementally, starting from two photographs and the points they observe.

## Slide 71: Incremental SFM
Slide by Seitz
Notes: We then add several photos at a time to the reconstruction, refine the model, and repeat until no more photos match any points in the scene.

## Slide 72: Photo Tourism overview
Scene reconstruction
Photo Explorer
Input photographs
Slide by Seitz
Notes: Once we reconstruct a scene, we can view it in our photo explorer. I’ll now describe the explore, starting with a demo of the system.

## Slide 73: Photo Explorer
Slide by Seitz

## Slide 74: Summary
Projection models:
  Perspective & Weak perspective
Algebraic formulation:
  Projective geometry
Tasks:
  Stereo
  Homograph
  SFM

## Slide 75: Stereo SC